## Slide 1: The Zebra Distributed routing software
Kunihiro Ishiguro
Digital Magic Labs, Inc.

## Slide 2: What’s Zebra ?
Zebra is a distributed multi-server multi-thread routing software.
Zebra is a free software distributed under GPL.
Modularity,extensibility,maintainability
It provides user level packet forwarding table when working with GNU Hurd.

## Slide 3: Why do we need yet another routing software?
Routed
Gated
MRT
Vender development software…..

## Slide 4: New world with zebra
One process per one protocol
kernel routing table update and redistribution between different protocols are provided by zebra daemon
Other daemons are for protocol handling
Easy to add a new protocol daemon
BGP route server and route reflector are integrated into BGPd

## Slide 5
Zebra architecture
BGPd
RIPd
OSPFd
zebra
UNIX Kernel

## Slide 6: Benefits of multiple server
It increases modularity, extensibility, maintainability
It allows incremental development of a protocol daemon
Easy to add a new protocol without changing other source codes
Often easy to debug

## Slide 7: Multiple servers can be slow
Inter process communication V.S. intra process communication
kernel routing table updates and redistribution would be slow
Authentication problem

## Slide 8
Zebra architecture on GNU Hurd
pfinet
RIPd
OSPFd
zebra
Mach Kernel
BGPd
lookup
answer

## Slide 9: Benefits of user level routing table
Source IP Address (and destination) based policy routing
per interface routing table
and much more ideas….
R
Segment 1
Segment 2

## Slide 10: zebra daemon
Wrapping service around interfaces
Kernel routing table updates
Redistribute routing information between different protocols

## Slide 11: Zebra API
ZEBRA_ROUTE_ADD
ZEBRA_ROUTE_DELTE
ZEBRA_ROUTE_LOOKUP
ZEBRA_INTERFACE_ALL
…

## Slide 12: RIPd
RIP Version1, 2 RIPng supports

## Slide 13: BGPd
BPG-4
Route server
Route reflector
Route flap dampening

## Slide 14: OSPFd and other
It’s time to develop other protocols

## Slide 15: Problems
Authentication
Performance
Each daemon has their own terminal interface and configuration file

## Slide 16: Current status
zebra(for *BSD),RIPd,BGPd(dump only) works
Zebra ML <zebra@digital-magic.co.jp> for subscription please write to <zebra-request@digital-magic.co.jp>
Zebra Home Page http://zebra.digital-magic.co.jp/